## Slide 1: Digital Design & Computer Arch. Lecture 16a: Dataflow & Superscalar Execution
Prof. Onur Mutlu
ETH Zürich
Spring 2020
23 April 2020

## Slide 2: Required Readings
This week
  Smith and Sohi, “The Microarchitecture of Superscalar Processors,” Proceedings of the IEEE, 1995
  H&H Chapters 7.8 and 7.9
  McFarling, “Combining Branch Predictors,” DEC WRL Technical Report, 1993.

## Slide 3: Agenda for Today & Next Few Lectures
Single-cycle Microarchitectures
Multi-cycle and Microprogrammed Microarchitectures
Pipelining
Issues in Pipelining: Control & Data Dependence Handling, State Maintenance and Recovery, …
Out-of-Order Execution
Other Execution Paradigms

## Slide 4: Recall: OOO Execution: Restricted Dataflow
An out-of-order engine dynamically builds the dataflow graph of a piece of the program
The dataflow graph is limited to the instruction window
  Instruction window: all decoded but not yet retired instructions
Can we do it for the whole program?
  In other words, how can we have a large instruction window?
Can we do it efficiently with Tomasulo’s algorithm?

## Slide 5: Recall: State of RAT and RS in Cycle 7
+
∗
E5
7
-
E3
E2
-
D
E4
6
-
E2
E1
D
F
E3
5
-
E1
D
F
E2
4
-
D
F
E1
3
D
F
D
2
F
F
1
Cycle
MUL | R1, R2 |  | R3
ADD | R3, R4 |  | R5
ADD | R2, R6 |  | R7
ADD | R8, R9 |  | R10
MUL | R7, R10 |  | R11
ADD | R5, R11 |  | R5
Register | Valid | Tag | Value
R1 | 1 |  | 1
R2 | 1 |  | 2
R3 | 0 | x | 
R4 | 1 |  | 4
R5 | 0 | a | 
R6 | 1 |  | 6
R7 | 0 | b | 
R8 | 1 |  | 8
R9 | 1 |  | 9
R10 | 0 | c | 
R11 | 0 | y | 
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
a | 0 | x |  | 1 | ~ | 4
b | 1 | ~ | 2 | 1 | ~ | 6
c | 1 | ~ | 8 | 1 | ~ | 9
d |  |  |  |  |  | 
0
a
0
y
0
d
 | Source 1 |  |  | Source 2 |  | 
 | V | Tag | Value | V | Tag | Value
x | 1 | ~ | 1 | 1 | ~ | 2
y | 0 | b |  | 0 | c | 
z |  |  |  |  |  | 
t |  |  |  |  |  | 

## Slide 6: Recall: Dataflow Graph

## Slide 7: Other Approaches to Concurrency (or Instruction Level Parallelism)

## Slide 8: Approaches to (Instruction-Level) Concurrency
Pipelining
Out-of-order execution
Dataflow (at the ISA level)
Superscalar Execution
VLIW
Fine-Grained Multithreading
SIMD Processing (Vector and array processors, GPUs)
Decoupled Access Execute
Systolic Arrays

## Slide 9: Review: Data Flow: Exploiting Irregular Parallelism

## Slide 10: Data Flow Summary
Availability of data determines order of execution
A data flow node fires when its sources are ready
Programs represented as data flow graphs (of nodes)
Data Flow at the ISA level has not been (as) successful
Data Flow implementations at the microarchitecture level (while preserving Von Neumann semantics) have been very successful
  Out of order execution is the prime example

## Slide 11: Pure Data Flow Advantages/Disadvantages
Advantages
  Very good at exploiting irregular parallelism
  Only real dependencies constrain processing
  More parallelism can be exposed than Von Neumann model
Disadvantages
  No precise state semantics
    Debugging very difficult
    Interrupt/exception handling is difficult (what is precise state semantics?)
  Too much parallelism? (Parallelism control needed)
  High bookkeeping overhead (tag matching, data storage)
  …

## Slide 12: Approaches to (Instruction-Level) Concurrency
Pipelining
Out-of-order execution
Dataflow (at the ISA level)
Superscalar Execution
VLIW
Fine-Grained Multithreading
SIMD Processing (Vector and array processors, GPUs)
Decoupled Access Execute
Systolic Arrays

## Slide 13: Superscalar Execution

## Slide 14: Superscalar Execution
Idea: Fetch, decode, execute, retire multiple instructions per cycle
  N-wide superscalar  N instructions per cycle
Need to add the hardware resources for doing so
Hardware performs the dependence checking between concurrently-fetched instructions
Superscalar execution and out-of-order execution are orthogonal concepts
  Can have all four combinations of processors:
    [in-order, out-of-order] x [scalar, superscalar]

## Slide 15: In-Order Superscalar Processor Example
Multiple copies of datapath: Can fetch/decode/execute multiple instructions per cycle
Dependencies make it tricky to issue multiple instructions at once
Here: Ideal IPC = 2

## Slide 16: In-Order Superscalar Performance Example
lw $t0, 40($s0)
add $t1, $s1, $s2
sub $t2, $s1, $s3 and $t3, $s3, $s4 or $t4, $s1, $s5
sw $s5, 80($s0)
Ideal IPC = 2
Actual IPC = 2 (6 instructions issued in 3 cycles)

## Slide 17: Superscalar Performance with Dependencies
lw $t0, 40($s0)
add $t1, $t0, $s1
sub $t0, $s2, $s3 and $t2, $s4, $t0 or $t3, $s5, $s6
sw $s7, 80($t3)
Ideal IPC = 2
Actual IPC = 1.2 (6 instructions issued in 5 cycles)

## Slide 18: Superscalar Execution Tradeoffs
Advantages
  Higher IPC (instructions per cycle)
Disadvantages
  Higher complexity for dependency checking
    Require checking within a pipeline stage
    Renaming becomes more complex in an OoO processor
  More hardware resources needed

## Slide 19: Digital Design & Computer Arch. Lecture 16a: Dataflow & Superscalar Execution
Prof. Onur Mutlu
ETH Zürich
Spring 2020
23 April 2020